## Slide 1
From Sensors to
Smart Systems
An Introduction
to ESP32 and IoT

## Slide 2
PART 1 · INTRODUCTION · THE RECURRING CHALLENGE
How could a small chip detect an ambulance
and change a traffic signal?
Sound · microphone
Light · LDR
Button · simulation
DECIDE
Enough evidence to act?
ACT
Change the signal
WAIT
Keep watching
What could fool a sound-only detector?
What evidence would you trust before acting?
A loud sound is a clue, not an identity, the system must decide before it acts.

## Slide 3
PART 1 · INTRODUCTION · YOUR LEARNING JOURNEY
One story for every project : sense, decide, act, communicate.
01
Sense
Read an input: button, LDR, microphone
02
Decide
Apply a rule: a threshold or condition
03
Act
Drive an output: LED, buzzer, servo
04
Communicate
Share a useful status: display, Wi-Fi
TRAFFIC SIGNAL MODEL
Button (simulated ambulance) → Rule → LED pattern changes → Status shared
SMART ALARM
Potentiometer threshold → Rule → Buzzer sounds → Reading shown on a display

## Slide 4
PART 1 · INTRODUCTION · HOW CAN A SMALL DEVICE DO SO MUCH?
Microcontrollers: Built for One Task, Computers for Many
MICROCONTROLLER · ESP32
The dedicated lab assistant
JOB
Runs one focused program, all the time
TALKS TO
Sensors and actuators, through its pins
LIVES
Inside a doorbell, a washer, a traffic controller
GENERAL-PURPOSE COMPUTER
The whole student workspace
JOB
Runs many applications for a person
TALKS TO
Screens, keyboards, networks, storage
LIVES
On a desk, in a data centre, in your bag
Both compute. They differ in role, integration and resources.

## Slide 5
PART 2 · ESP32 · INSTRUCTIONS, MEMORY, I/O, PROTOCOLS, RADIOS
The ESP32 is the brain: processor, memory,
pins, ADC and radios in one module.
ESP32 MODULE · FUNCTIONAL VIEW
CPU
1–2 cores*
RAM
working data
FLASH
program store
GPIO
digital I/O
ADC
analog input
RADIO
Wi-Fi · BT
GPIO header pins — count and numbering vary by board
Pins also carry UART · I2C · SPI; radios add Wi-Fi and Bluetooth*

## Slide 6
PART 2 · ESP32 · INSTRUCTIONS · RISC AND CISC
The CPU repeats a tiny cycle
fetch an instruction, decode it and execute it.
FETCH
Get the next instruction
DECODE
Work out what it means
EXECUTE
Do it: read, compare, write
RISC · SMALL SPECIALISED STEPS
LOAD R1, GPIO ; Read GPIO register
OR R1, R1, #0x20 ; Set bit 5
STORE GPIO, R1 ; Write it back
CISC · COMPLEX COMBINED STEPS
ESP32 variants use Xtensa or RISC-V cores. This is a way of thinking, not a speed ranking.
BSET GPIO, 5 ; Set GPIO bit 5

## Slide 7
PART 2 · ESP32 · TYPES OF MEMORY
If power goes off, which memory keeps its contents?
power on
power off
later
FLASH · NOTEBOOK
Program code
kept
RAM · WORKTABLE
Live variables
lost
NVS · LOCKER
Saved settings (in flash)
kept
PREDICT · SHOW OF HANDS
A counter in RAM or an alarm threshold saved to NVS, which survives?
NVS lives in flash, it survives resets but has limited write cycles and saves deliberately.

## Slide 8
PART 3 · INPUT DEVICES · PUSH BUTTON AND PULL-UP RESISTORS
What does a pin read when nothing is connected?
FLOATING · NO RESISTOR
?
GPIO
Reads: unpredictable
Noise decides the level.
PULL-UP
3.3 V
R
GPIO
idle: HIGH
pressed: LOW
GND
PULL-DOWN
3.3 V
R
GPIO
idle: LOW
pressed: HIGH
GND
A pull resistor keeps the pin at a steady default level when nothing is happening. But when you press the button, that action takes control and changes the pin’s state.

## Slide 9
PART 3 · INPUT DEVICES · LDR, MICROPHONE, ULTRASONIC, DHT
Sensors: Each Measures a Unique Quantity in Its Own Electrical Form

## Slide 10
PART 4 · OUTPUT DEVICES · LED, BUZZER, OLED, SERVO
Outputs turn a decision into something
people can see, hear or feel.

## Slide 11
PART 5 · ARDUINO STRUCTURE · void setup() AND void loop()
setup() prepares the stage once & loop() repeats the performance.
blink.ino
void setup() {
pinMode(LED_PIN, OUTPUT); // once
}
void loop() {
digitalWrite(LED_PIN, HIGH); // on
delay(500);
digitalWrite(LED_PIN, LOW); // off
delay(500);
}
setup() · RUNS ONCE
Prepare the stage: pin modes, serial, sensors
loop() · REPEATS FOREVER
The performance: read → decide → act, again and again
↺ returns to the top of loop()
PREDICT
What does the LED do?
What changes with delay(100)?
LED_PIN is defined for your verified board and external LED circuit

## Slide 12
PART 6 · GPIO · ENABLING A PIN, READING AND WRITING
Digital input reads a button & digital output drives an LED.
Digital input — pressed or released
Digital output — on or off
ESP32
read → decide → drive
HIGH / LOW in
HIGH / LOW out
Before power: check LED polarity, the resistor, 3.3 V logic levels and a shared ground.
GPIO pin
Resistor
LED (+ → −)
GND
ENABLE · READ · WRITE
pinMode(BUTTON_PIN, INPUT_PULLUP);
pinMode(LED_PIN, OUTPUT);
bool on = digitalRead(BUTTON_PIN) == LOW;
digitalWrite(LED_PIN, on ? HIGH : LOW);
OUTPUT CIRCUIT · CONCEPT, NOT A WIRING MAP

## Slide 13
PART 6 · ANALOG PIN · READING VALUES WITH THE ADC
The ADC turns a changing voltage into a number.
PLACEHOLDER
Potentiometer
PLACEHOLDER
LDR module
voltage
time
ADC READING · EXAMPLE
2048
analogRead() → 0…4095 (12-bit)
low voltage → small number
high voltage → large number
Readings are steps and can be noisy. AnalogReadMilliVolts() returns calibrated millivolts.
v = analogRead(POT_PIN);

## Slide 14
PART 7 · COMMUNICATION PROTOCOLS
Wired Protocols: Choose the One Your Device Speaks
UART · THE DIRECT SHUTTLE
TX
RX
WIRES · 2 (TX, RX)
USE · text to your laptop
KIT · Serial Monitor**
I2C · THE ADDRESSED BUS
SDA
SCL
WIRES · 2 (SDA, SCL), shared
USE · many addressed devices
KIT · OLED / LCD adapter
SPI · THE EXPRESS LANE
WIRES · 4 (SCK, MOSI, MISO, CS)
USE · fast displays, SD cards
KIT · SPI display, if supplied
WIRELESS
Wi-Fi: link to a web page or cloud service. Bluetooth: pair with nearby devices.
Radio support varies by ESP32 variant.

## Slide 15
PART 8 · COMPILATION PROCESS
Your text becomes machine instructions
before the ESP32 can run it.
01 SOURCE
Your sketch: readable text
02 COMPILE
Toolchain translates + links
03 BINARY
Machine code for the ESP32 cores
04 UPLOAD
Sent over USB into flash
05 EXECUTE
Board resets and runs it
IF THE BUILD FAILS
Read the first error line; fix the source or the board selection.
IF THE UPLOAD FAILS
Check the cable (data, not charge-only), the port and the board selection.

## Slide 16
PART 9 · DEBUGGING · SERIAL MONITOR AND ALTERNATIVES
Investigate the physical system before you blame the code.
ASK IN ORDER
01
Is the board powered? (LED, USB, supply)
02
Are the connections correct? (pins, polarity, ground)
03
Is the expected code running? (right board, port, upload)
04
What does the Serial Monitor report? (baud rate matches)
SPOT THE BUG · 60 SECONDS
pinMode(LED_PIN, INPUT);
digitalWrite(LED_PIN, HIGH);
Wiring verified. Upload succeeded.
The LED never lights. Which word is wrong?
Disconnect power before rewiring. Serial output shows what the code sees, not whether wiring is safe.
SERIAL MONITOR · AND ALTERNATIVES
Serial.begin(115200);
Serial.println(reading);

## Slide 17
PART 10 · IOT BASICS AND INTRODUCTION
A connected device is only useful
if someone can act on what it shares.
SENSOR
Observe the world
ESP32
Decide locally
WI-FI
Carry the message
WEB / CLOUD
Show status, keep history
USER
Take action
LOCAL OUTPUT
Buzzer or LED still responds if Wi-Fi drops
Smart alarm: The buzzer sounds locally, the dashboard adds context.
Traffic model: Report the simulated event and never treat noise as authority.

## Slide 18
PART 11 · IOT ON THE ESP32 · SETTING UP A WEB SERVER
The ESP32 can serve a web page
that shows its own sensor reading.
webserver.ino · arduino-esp32
1 · JOIN THE NETWORK
WiFi.begin() joins the classroom Wi-Fi — or WiFi.softAP() makes the ESP32 its own hotspot.
2 · LISTEN ON PORT 80
WebServer waits for requests and the Serial Monitor prints the board's IP address.
3 · RESPOND
A laptop browser opens http://<board-ip>/ — the board replies with its live reading.
#include <WiFi.h>
#include <WebServer.h>
WebServer server(80);
void setup() {
WiFi.begin(SSID, PASSWORD);
while (WiFi.status() != WL_CONNECTED)
delay(500);
server.on("/", []() {
server.send(200, "text/plain",
String(analogRead(POT_PIN)));
});
server.begin();
}
void loop() { server.handleClient(); }

## Slide 19
The ESP32 can be connect to any APIs.