## Slide 1
INTERACTIVE WORKSHOP · ESP32 & IOT · 45 MINUTES
From Sensors to
Smart Systems
An Interactive Introduction
to ESP32 and IoT
OPENING QUESTION
How many computers did you
interact with before
reaching this room?
50 students · 10 teams of five · hands-on session follows
PHOTO PLACEHOLDER · 6 REAL PHOTOS · 4:3
Traffic light
Smartwatch
Washing machine
Car dashboard
Elevator panel
Smart speaker
Everyday objects that quietly contain microcontrollers
Notes: TIME: 2 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: How many computers did you interact with before reaching this room? KEY TAKEAWAY: Computing is hidden inside many familiar objects, not only laptops. DELIVERY: Quick show of hands, then students name objects from the gallery. Many such products contain microcontrollers; complex products can also contain other processors. Introduce the title as a workshop about making a physical system respond. INTERACTION / ANSWER: There is no fixed count. Traffic lights, washing machines, cars, smartwatches, elevators and smart speakers can contain embedded controllers. Do not claim every object has only one controller or is only a microcontroller. TRANSITION: Let's turn one familiar object into our recurring design problem. 1 VISUAL: the cover and closing backdrops are AI-generated abstract light textures — no hardware or components are depicted. The six-object collage remains a real-photo placeholder. 1 VISUAL: the cover and closing backdrops are AI-generated abstract light textures — no hardware or components are depicted. The six-object collage remains a real-photo placeholder. PHOTO PLACEHOLDER: Collage of six everyday objects (traffic light, smartwatch, washing machine, car dashboard, elevator panel, smart speaker) | Composition/crop: Six real photographs, 4:3 each, arranged 3 × 2 | Caption: Everyday objects that quietly contain microcontrollers | Suggested search: Collage of six everyday objects (traffic light, smartwatch, washing machine, car dashboard, elevator panel, smart speaker) | Recommended source: Licensed stock / verified CC or public-domain photos | Replace with actual workshop hardware: No. 1 ROADMAP (11 parts): 1 Introduction — microcontrollers · 2 ESP32: instructions, memory, I/O, protocols, radios · 3 Input devices · 4 Output devices · 5 Arduino structure · 6 GPIO and analog readings · 7 Communication protocols · 8 Compilation · 9 Debugging (Serial Monitor, alternatives) · 10 IoT basics · 11 A tiny web server on the ESP32.

## Slide 2
PART 1 · INTRODUCTION · THE RECURRING CHALLENGE
02 / 19
How could a small chip detect an ambulance
and change a traffic signal?
CANDIDATE EVIDENCE
Sound · microphone
Light · LDR
Button · simulation
DECIDE
Enough evidence to act?
ACT
Change the signal
WAIT
Keep watching
PAIR TALK · 30 SECONDS
What could fool a sound-only detector?
What evidence would you trust before acting?
Classroom tabletop model only.
A button safely simulates the event.
A loud sound is a clue, not an identity — the system must decide before it acts.
Notes: TIME: 2 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: How could a small chip detect an ambulance and change a traffic signal? KEY TAKEAWAY: A useful system needs evidence, a decision and a safe response. DELIVERY: Give pairs 30 seconds. Take two suggestions. Keep this a tabletop teaching model, never a road-control design. A microphone threshold can detect loudness, not reliably identify a siren or authenticate an emergency vehicle. A button can safely simulate the event during the workshop. INTERACTION / ANSWER: Accept ideas such as a simulated input or authenticated vehicle message. Loudness alone can be fooled by horns, music or other noise; reliable detection and real traffic control require validation and safety engineering. TRANSITION: Every suggestion can be organized into four simple verbs. 2 2 2 2

## Slide 3
PART 1 · INTRODUCTION · YOUR LEARNING JOURNEY
03 / 19
One story for every project: sense, decide, act, communicate.
01
Sense
Read an input: button, LDR, microphone
02
Decide
Apply a rule: a threshold or condition
03
Act
Drive an output: LED, buzzer, servo
04
Communicate
Share a useful status: display, Wi-Fi
TRAFFIC SIGNAL MODEL
Button (simulated ambulance) → rule → LED pattern changes → status shared
SMART ALARM
Potentiometer threshold → rule → buzzer sounds → reading shown on a display
Connectivity extends the loop; useful behaviour never depends on it.
Notes: TIME: 1.5 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: Which of these four verbs describes a button? Which describes a buzzer? KEY TAKEAWAY: Sense, decide and act form the local system; communication can extend it. DELIVERY: Point to the colour key: input blue, processing orange, output green, communication purple. Follow one traffic-model example and one smart-alarm example. These are functional roles, not exact wiring diagrams. INTERACTION / ANSWER: A button is an input: sense. A buzzer is an output: act. The program makes the decision. Sending a status update belongs to communicate. TRANSITION: What kind of computer can sit at the centre of a small system? 3 3 3 3

## Slide 4
PART 1 · INTRODUCTION · HOW CAN A SMALL DEVICE DO SO MUCH?
04 / 19
A microcontroller is built for one physical job;
a computer for many.
MICROCONTROLLER · ESP32
The dedicated lab assistant
JOB
Runs one focused program, all the time
TALKS TO
Sensors and actuators, through its pins
LIVES
Inside a doorbell, a washer, a traffic controller
GENERAL-PURPOSE COMPUTER
The whole student workspace
JOB
Runs many applications for a person
TALKS TO
Screens, keyboards, networks, storage
LIVES
On a desk, in a data centre, in your bag
Both compute. They differ in role, integration and resources — not in intelligence.
Notes: TIME: 2 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: Would you put a full laptop inside every doorbell? KEY TAKEAWAY: A microcontroller is designed to control a focused embedded job; a computer is typically more general-purpose. DELIVERY: Use the dedicated-assistant analogy without claiming microcontrollers can do only one thing. They can schedule several tasks or run an RTOS. Both have processors and memory; the distinction is integration, typical role and available resources, not intelligence. INTERACTION / ANSWER: A doorbell often needs a small controller, while development and editing are convenient on a general-purpose computer. More complex products may use both. TRANSITION: Our hands-on assistant is an ESP32 development board. TECHNICAL REFERENCES: Espressif, ESP32 Datasheet: https://documentation.espressif.com/esp32_datasheet_en.html 4 4 4 4

## Slide 5
PART 2 · ESP32 · INSTRUCTIONS, MEMORY, I/O, PROTOCOLS, RADIOS
05 / 19
The ESP32 is the brain: processor, memory,
pins, ADC and radios in one module.
PHOTO PLACEHOLDER
ESP32 development board — the exact kit model
Top-down · USB connector visible · space for callouts · 4:3
ESP32 MODULE · FUNCTIONAL VIEW
CPU
1–2 cores*
RAM
working data
FLASH
program store
GPIO
digital I/O
ADC
analog input
RADIO
Wi-Fi · BT*
GPIO header pins — count and numbering vary by board
*Cores, memory and Bluetooth support vary by ESP32 variant — a functional view, not a pin map.
Pins also carry UART · I2C · SPI; radios add Wi-Fi and Bluetooth*
Notes: TIME: 2.5 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: Where would you plug in the USB cable, and where would you connect a sensor? KEY TAKEAWAY: The development board exposes a programmable ESP32 plus interfaces and supporting power circuitry. DELIVERY: Use the actual board in the room. Identify USB connector, module, GPIO headers, antenna area and power section only after matching the board photograph. CPU, memory and peripherals are functional blocks, not necessarily individually visible chips. Board features, antenna style, flash arrangement and wireless capabilities vary. INTERACTION / ANSWER: USB and GPIO locations must be verified on the exact board. Some variants lack Bluetooth; Bluetooth Classic and BLE support also vary. Do not label an unknown pin or promise exact CPU, memory or ADC specifications. TRANSITION: Now zoom into the processor: what does it actually do? TECHNICAL REFERENCES: Espressif, Chip Series Comparison: https://docs.espressif.com/projects/esp-idf/en/v5.0-rc1/esp32/hw-reference/chip-series-comparison.html Espressif, ESP32 Datasheet: https://documentation.espressif.com/esp32_datasheet_en.html 5 5 PHOTO PLACEHOLDER: ESP32 development board — the exact kit model | Composition/crop: Top-down · USB connector visible · space for callouts · 4:3 | Caption: ESP32 development board | Suggested search: ESP32 development board — the exact kit model | Recommended source: Own photo of the actual kit component | Replace with actual workshop hardware: Yes. 5

## Slide 6
PART 2 · ESP32 · INSTRUCTIONS · RISC AND CISC
06 / 19
The CPU repeats a tiny cycle:
fetch an instruction, decode it, execute it.
FETCH
Get the next instruction
DECODE
Work out what it means
EXECUTE
Do it: read, compare, write
…then repeat, millions of times each second
RISC · SMALL SPECIALISED STEPS
pick up → move → place
Many simple instructions, each quick to decode.
CISC · COMPLEX COMBINED STEPS
make the sandwich
Fewer, richer instructions that bundle several steps.
ESP32 variants use Xtensa or RISC-V cores. This is a way of thinking, not a speed ranking.
Notes: TIME: 2 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: If I say 'make a sandwich', how many smaller actions might be hidden inside it? KEY TAKEAWAY: Programs eventually become machine instructions that the processor executes. DELIVERY: Describe fetch, decode and execute as a conceptual cycle, not a literal timing model. RISC favours simpler reusable instruction building blocks; CISC provides richer combined operations. This analogy is not a speed ranking and modern implementations blur simple comparisons. ESP32-family variants use Xtensa or RISC-V; the original ESP32 and ESP32-C3 are different examples. INTERACTION / ANSWER: Many smaller steps are possible. One source-code statement is not necessarily one machine instruction, and RISC does not mean every instruction always completes in one clock cycle. TRANSITION: Those instructions need somewhere to live and somewhere to work. TECHNICAL REFERENCES: Espressif, Chip Series Comparison: https://docs.espressif.com/projects/esp-idf/en/v5.0-rc1/esp32/hw-reference/chip-series-comparison.html 6 6 6 6

## Slide 7
PART 2 · ESP32 · TYPES OF MEMORY
07 / 19
Power goes off. Which memory keeps its contents?
power on
power off
later
FLASH · NOTEBOOK
Program code
kept
RAM · WORKTABLE
Live variables
lost
NVS · LOCKER
Saved settings (in flash)
kept
PREDICT · SHOW OF HANDS
A counter in RAM or an alarm threshold saved to NVS — which survives?
NVS lives in flash: it survives resets but has limited write cycles — save deliberately.
Notes: TIME: 2.5 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: Your worktable gets cleared overnight. What survives in your notebook or locker? KEY TAKEAWAY: Working RAM is volatile; program flash and explicitly saved non-volatile settings persist. DELIVERY: Ask students to vote before giving the answer. Flash is the program notebook. RAM is the temporary worktable. NVS is the locker abstraction, commonly backed by flash; it is not necessarily a third physical memory chip. A variable does not become persistent merely because it has a meaningful name. INTERACTION / ANSWER: The explicitly saved threshold survives if it was successfully written to non-volatile storage. An ordinary changing RAM counter does not. Avoid saving on every loop iteration; flash has finite write endurance. TRANSITION: Memory holds the program and its settings. Now to what feeds it: the inputs, starting with the humble push button. TECHNICAL REFERENCES: Espressif, Non-Volatile Storage Library: https://docs.espressif.com/projects/esp-idf/en/stable/esp32/api-reference/storage/nvs_flash.html Espressif, ESP32 Datasheet: https://documentation.espressif.com/esp32_datasheet_en.html 7 7 7 7

## Slide 8
PART 3 · INPUT DEVICES · PUSH BUTTON AND PULL-UP RESISTORS
08 / 19
What does a pin read when nothing is connected?
FLOATING · NO RESISTOR
?
GPIO
Reads: unpredictable
Noise decides the level.
PULL-UP
3.3 V
R
GPIO
idle: HIGH
pressed: LOW
GND
PULL-DOWN
3.3 V
R
GPIO
idle: LOW
pressed: HIGH
GND
Reveal: a pull resistor gives the pin a defined idle level; pressing the button overrides it.
Many pins offer internal pulls (INPUT_PULLUP / INPUT_PULLDOWN) — check your board's pin notes.
Notes: TIME: 2.5 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: Hands up: will an unconnected input always read LOW, always HIGH, or fluctuate? KEY TAKEAWAY: Floating inputs lack a defined level; pull resistors set a default state while a button can override it. DELIVERY: Wait for predictions. The diagrams show the logical branches, using a resistor symbol and a labelled button location; these are conceptual, not a breadboard wiring map. Pull-up: resistor to 3.3 V and button to ground. Pull-down: button to 3.3 V and resistor to ground. A pressed button closes its branch. No direct short between supply and ground is intended. INTERACTION / ANSWER: It can read unpredictably due to noise and leakage; it need not visibly toggle on every read. Pull-up gives idle HIGH/pressed LOW, while pull-down gives idle LOW/pressed HIGH. Internal pull availability and special pin restrictions vary. Software debouncing is a separate issue. TRANSITION: A button gives a clean logic level. Other sensors in the kit report in different ways — let's tour them. TECHNICAL REFERENCES: Espressif, Arduino-ESP32 GPIO API: https://docs.espressif.com/projects/arduino-esp32/en/latest/api/gpio.html 9 9 9 9

## Slide 9
PART 3 · INPUT DEVICES · LDR, MICROPHONE, ULTRASONIC, DHT
09 / 19
Each sensor reports a different quantity —
and in a different electrical form.
PLACEHOLDER
Top-down · legs visible
Push button
Press / release
Digital level
PLACEHOLDER
Top-down · LDR visible
LDR module
Light level
Analog voltage*
PLACEHOLDER
Top-down · mic visible
Microphone module
Sound level
Analog/digital*
PLACEHOLDER
Front · transducers visible
Ultrasonic sensor
Distance by echo
Timed pulse†
PLACEHOLDER
Front · connector visible
DHT sensor
Temp. + humidity
Data protocol
QUICK CHECK
Which sensors give a smoothly changing number? Which give yes / no?
*Module-dependent. †HC-SR04 echo is 5 V logic — divide or level-shift before an ESP32 pin.
Notes: TIME: 2.5 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: Which of these detects a physical quantity, and which provides a communication protocol? KEY TAKEAWAY: A physical quantity and an electrical output type are different things. DELIVERY: Point to actual kit parts. A button is a discrete input. An LDR element is a light-dependent resistor, and its module may expose analog and/or thresholded digital output. Microphone modules may provide analog audio, a digital threshold, or a digital audio interface. HC-SR04-style ultrasonic modules use trigger/echo timing; other models differ. DHT devices return temperature and humidity over a model-specific digital data protocol. INTERACTION / ANSWER: The quantity is what is observed, such as light or temperature. Analog, digital level, timed pulse and protocol describe how that observation reaches the controller. Never assume all sensors are analog. Standard HC-SR04 echo signals commonly need voltage compatibility checking/level shifting for ESP32. Exact workshop modules are unknown; placeholders intentionally request their photographs. TRANSITION: Observations become useful when the system can respond. TECHNICAL REFERENCES: Espressif, Arduino-ESP32 GPIO API: https://docs.espressif.com/projects/arduino-esp32/en/latest/api/gpio.html Espressif, Arduino-ESP32 ADC API: https://docs.espressif.com/projects/arduino-esp32/en/latest/api/adc.html 11 11 PHOTO PLACEHOLDER: Push button | Composition/crop: Top-down · legs visible · 4:3 | Caption: Push button | Suggested search: Push button | Recommended source: Own photo of the actual kit component | Replace with actual workshop hardware: Yes. PHOTO PLACEHOLDER: LDR module | Composition/crop: Top-down · LDR visible · 4:3 | Caption: LDR module | Suggested search: LDR module | Recommended source: Own photo of the actual kit component | Replace with actual workshop hardware: Yes. PHOTO PLACEHOLDER: Microphone module | Composition/crop: Top-down · mic visible · 4:3 | Caption: Microphone module | Suggested search: Microphone module | Recommended source: Own photo of the actual kit component | Replace with actual workshop hardware: Yes. PHOTO PLACEHOLDER: Ultrasonic sensor | Composition/crop: Front · transducers visible · 4:3 | Caption: Ultrasonic sensor | Suggested search: Ultrasonic sensor | Recommended source: Own photo of the actual kit component | Replace with actual workshop hardware: Yes. PHOTO PLACEHOLDER: DHT sensor | Composition/crop: Front · connector visible · 4:3 | Caption: DHT sensor | Suggested search: DHT sensor | Recommended source: Own photo of the actual kit component | Replace with actual workshop hardware: Yes. 11

## Slide 10
PART 4 · OUTPUT DEVICES · LED, BUZZER, OLED, SERVO
10 / 19
Outputs turn a decision into something
people can see, hear or feel.
PLACEHOLDER
Macro · both leads visible · 4:3
LED
Status light
DRIVE
digitalWrite() or PWM
PLACEHOLDER
Top-down · connector visible · 4:3
Buzzer
Alarm tone
DRIVE
tone() or PWM pulses
PLACEHOLDER
Front · whole module visible · 4:3
OLED display
Live readings and text
DRIVE
I2C library (e.g. SSD1306)
PLACEHOLDER
Side · horn and cable visible · 4:3
Micro servo
Moves a gate or pointer
DRIVE
PWM servo library · 5 V*
Match the output to the problem: what should a person notice, and how quickly?
*Servos need their own power; a GPIO pin carries the decision, not the current. Kits may also include a 16×2 LCD or relay module — same rule.
Notes: TIME: 2 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: Which output would make our smart alarm noticeable without looking at a screen? KEY TAKEAWAY: Outputs display, sound, switch or move in response to a decision. DELIVERY: A buzzer makes an audible alarm; an LED indicates status; the OLED shows readings and text; a servo moves a gate or pointer. LCD and relay modules, if present in a kit, follow the same rules. Distinguish displays/indicators from motion actuators. Active versus passive buzzers need different drive patterns. A relay coil generally needs a driver and protection unless provided on a compatible module. INTERACTION / ANSWER: A buzzer is a natural alarm output, perhaps with an LED or display for redundancy. Servo motors and some other outputs require a suitable power source or driver; GPIO cannot supply motor current. Respect device ratings and voltage compatibility, use a shared reference ground where the non-isolated circuit requires it, and keep the workshop low-voltage: no mains switching. TRANSITION: How do we express this behaviour in a tiny program? TECHNICAL REFERENCES: Espressif, ESP32 Datasheet: https://documentation.espressif.com/esp32_datasheet_en.html 12 12 PHOTO PLACEHOLDER: LED | Composition/crop: Macro · both leads · 4:3 | Caption: LED | Suggested search: LED | Recommended source: Own photo of the actual kit component | Replace with actual workshop hardware: Yes. PHOTO PLACEHOLDER: Buzzer | Composition/crop: Top-down · connector · 4:3 | Caption: Buzzer | Suggested search: Buzzer | Recommended source: Own photo of the actual kit component | Replace with actual workshop hardware: Yes. PHOTO PLACEHOLDER: OLED display | Composition/crop: Front · whole module · 4:3 | Caption: OLED display | Suggested search: OLED display | Recommended source: Own photo of the actual kit component | Replace with actual workshop hardware: Yes. PHOTO PLACEHOLDER: Micro servo | Composition/crop: Side · horn + cable · 4:3 | Caption: Micro servo | Suggested search: Micro servo | Recommended source: Own photo of the actual kit component | Replace with actual workshop hardware: Yes. 12

## Slide 11
PART 5 · ARDUINO STRUCTURE · void setup() AND void loop()
11 / 19
setup() prepares the stage once; loop() repeats the performance.
blink.ino
void setup() {
pinMode(LED_PIN, OUTPUT); // once
}
void loop() {
digitalWrite(LED_PIN, HIGH); // on
delay(500);
digitalWrite(LED_PIN, LOW); // off
delay(500);
}
setup() · RUNS ONCE
Prepare the stage: pin modes, serial, sensors
loop() · REPEATS FOREVER
The performance: read → decide → act, again and again
↺ returns to the top of loop()
PREDICT
What does the LED do?
What changes with delay(100)?
LED_PIN is defined for your verified board and external LED circuit — no pin numbers are assumed here.
Notes: TIME: 2.5 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: If setup is preparing the stage, which part is the performance that keeps repeating? KEY TAKEAWAY: Arduino runs setup once after startup/reset, then repeats loop. DELIVERY: Read nine lines from top to bottom. This excerpt assumes the facilitator has already defined LED_PIN for a verified external LED circuit. Do not invent or copy a pin number from another board. Use a current-limiting resistor, correct polarity and a safe GPIO. delay takes milliseconds and is intentionally simple; it blocks this loop's progress, so later projects can use elapsed-time logic. INTERACTION / ANSWER: For the shown active-high external LED circuit: on for 500 ms, then off for 500 ms, repeating. Some onboard LEDs are active-low or addressable and need a different example. pinMode belongs in setup for this unchanged pin configuration. The excerpt is not a complete board-specific sketch until LED_PIN is defined. TRANSITION: Now put real pins into setup() and loop(): enable a GPIO, read it, drive it. TECHNICAL REFERENCES: Espressif, Arduino-ESP32 GPIO API: https://docs.espressif.com/projects/arduino-esp32/en/latest/api/gpio.html 13 13 Code panel: 10 lines including comments. LED_PIN must be defined for the verified board and external LED circuit. 13 Code panel: 10 lines including comments. LED_PIN must be defined for the verified board and external LED circuit. 13

## Slide 12
PART 6 · GPIO · ENABLING A PIN, READING AND WRITING
12 / 19
Digital input reads a button; digital output drives an LED.
PLACEHOLDER
Push button
PLACEHOLDER
LED
Digital input — pressed or released
Digital output — on or off
ESP32
read → decide → drive
HIGH / LOW in
HIGH / LOW out
Before power: check LED polarity, the resistor, 3.3 V logic levels and a shared ground.
GPIO pin
Resistor
LED (+ → −)
GND
ENABLE · READ · WRITE
pinMode(BUTTON_PIN, INPUT_PULLUP);
pinMode(LED_PIN, OUTPUT);
bool on = digitalRead(BUTTON_PIN) == LOW;
digitalWrite(LED_PIN, on ? HIGH : LOW);
OUTPUT CIRCUIT · CONCEPT, NOT A WIRING MAP
pinMode enables · digitalRead samples · digitalWrite drives
Notes: TIME: 2.5 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: Which direction does information travel when you press a button? KEY TAKEAWAY: Digital input reads HIGH/LOW; digital output drives a supported HIGH/LOW level. DELIVERY: Trace the information arrows; they are not wiring instructions. Use a current-limiting resistor with a bare LED. Check LED polarity, shared reference ground, allowed voltage and current before power-up. ESP32 GPIO must not be assumed 5 V tolerant. Verify safe pins against the exact development board. INTERACTION / ANSWER: Information goes from the pressed button to the program, then from the program to the LED output. The meaning of HIGH or LOW depends on the circuit; a pull-up button commonly reads LOW when pressed. TRANSITION: Digital pins give HIGH or LOW. Analog pins give a number — let's read one. TECHNICAL REFERENCES: Espressif, Arduino-ESP32 GPIO API: https://docs.espressif.com/projects/arduino-esp32/en/latest/api/gpio.html Espressif, ESP32 Datasheet: https://documentation.espressif.com/esp32_datasheet_en.html 8 8 PHOTO PLACEHOLDER: Push button | Composition/crop: Top-down · legs visible · 4:3 | Caption: Push button | Suggested search: Push button | Recommended source: Own photo of the actual kit component | Replace with actual workshop hardware: Yes. PHOTO PLACEHOLDER: LED | Composition/crop: Macro · both leads visible · 4:3 | Caption: LED | Suggested search: LED | Recommended source: Own photo of the actual kit component | Replace with actual workshop hardware: Yes. 8 CODE: pinMode() enables a pin as input (with INPUT_PULLUP where supported) or output; digitalRead() returns HIGH/LOW; digitalWrite() sets the output level. BUTTON_PIN and LED_PIN are defined for the verified board.

## Slide 13
PART 6 · ANALOG PIN · READING VALUES WITH THE ADC
13 / 19
The ADC turns a changing voltage into a number.
PLACEHOLDER
Potentiometer
PLACEHOLDER
LDR module
voltage
time
ADC READING · EXAMPLE
2048
analogRead() → 0…4095 (12-bit)
low voltage → small number
high voltage → large number
GUESS THE READING
Knob at the middle — guess the number. Turn it to the end — now?
Readings are steps and can be noisy; analogReadMilliVolts() returns calibrated millivolts.
v = analogRead(POT_PIN);
Notes: TIME: 2.5 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: Imagine slowly turning a volume knob. Does the physical position jump between only two states? KEY TAKEAWAY: An ADC samples an analog voltage and represents it with a finite digital code. DELIVERY: Use a potentiometer voltage example for the prediction. More input voltage generally means a higher ADC code within its valid configured range; readings are finite steps, can be noisy, and are not automatically calibrated physical units. State that the central sequence is a qualitative signal visualization, not measured data. An LDR changes resistance; a circuit converts that into a voltage. Module outputs may include analog and/or a thresholded digital output. INTERACTION / ANSWER: For the potentiometer input voltage described, the answer is a higher code. Do not promise an exact maximum value, reference voltage, linearity, resolution, or that clockwise always increases the voltage. Brightness-to-code direction depends on the divider or module circuit. TRANSITION: Single pins carry levels and voltages. Richer devices exchange messages — protocols next. TECHNICAL REFERENCES: Espressif, Arduino-ESP32 ADC API: https://docs.espressif.com/projects/arduino-esp32/en/latest/api/adc.html 10 The ADC readout '2048' is an illustrative example only; Arduino-ESP32 defaults to 12-bit readings (0–4095), configurable. 10 The ADC readout '2048' is an illustrative example only; Arduino-ESP32 defaults to 12-bit readings (0–4095), configurable. PHOTO PLACEHOLDER: Potentiometer | Composition/crop: Three-quarter view · shaft and terminals visible · 4:3 | Caption: Potentiometer | Suggested search: Potentiometer | Recommended source: Own photo of the actual kit component | Replace with actual workshop hardware: Yes. PHOTO PLACEHOLDER: LDR module | Composition/crop: Top-down · sensor and connector visible · 4:3 | Caption: LDR module | Suggested search: LDR module | Recommended source: Own photo of the actual kit component | Replace with actual workshop hardware: Yes. 10 CODE: analogRead(pin) returns the raw ADC code, 0–4095 at the 12-bit default; analogReadMilliVolts(pin) returns calibrated millivolts. Only ADC-capable pins work, and some are unavailable while Wi-Fi is active.

## Slide 14
PART 7 · COMMUNICATION PROTOCOLS
14 / 19
Wired protocols are transport systems:
pick the one your device speaks.
UART · THE DIRECT SHUTTLE
TX
RX
WIRES · 2 (TX, RX)
USE · text to your laptop
KIT · Serial Monitor**
I2C · THE ADDRESSED BUS
SDA
SCL
WIRES · 2 (SDA, SCL), shared
USE · many addressed devices
KIT · OLED / LCD adapter
SPI · THE EXPRESS LANE
WIRES · 4 (SCK, MOSI, MISO, CS)
USE · fast displays, SD cards
KIT · SPI display, if supplied
WIRELESS
Wi-Fi: link to a web page or cloud service. Bluetooth: pair with nearby devices.
Radio support varies by ESP32 variant.
*Counts exclude power and ground. **Many boards route Serial over USB through a bridge chip.
Notes: TIME: 2.5 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: Would you use a direct shuttle, an addressed bus, or a selected express lane? KEY TAKEAWAY: Communication protocols define how devices exchange data; the hardware must support the same interface. DELIVERY: UART commonly uses two signal lines, TX and RX, plus a shared reference ground. I2C commonly uses two shared signal lines, SDA and SCL, with pull-ups and device addresses. Conventional SPI commonly uses SCK, MOSI, MISO and a device-select line; additional devices often need additional selects, and some devices omit a return signal. Counts exclude power and ground. Analog signals and digital levels are not interchangeable with these message protocols. INTERACTION / ANSWER: Use the interface documented for the exact module, not its appearance. OLED/LCD modules may have I2C, SPI or other interfaces. Many development boards expose serial via a USB-UART bridge; others use native USB, so Serial Monitor is not proof that external UART wires are present. Wi-Fi and Bluetooth are wireless options, but not all ESP32 variants support the same radios. TRANSITION: Your laptop must translate the source code before the board can execute it. TECHNICAL REFERENCES: Espressif, I2C API: https://docs.espressif.com/projects/esp-idf/en/stable/esp32/api-reference/peripherals/i2c.html Espressif, Chip Series Comparison: https://docs.espressif.com/projects/esp-idf/en/v5.0-rc1/esp32/hw-reference/chip-series-comparison.html 14 14 14 14

## Slide 15
PART 8 · COMPILATION PROCESS
15 / 19
Your text becomes machine instructions
before the ESP32 can run it.
01 SOURCE
Your sketch: readable text
02 COMPILE
Toolchain translates + links
03 BINARY
Machine code for the ESP32 cores
04 UPLOAD
Sent over USB into flash
05 EXECUTE
Board resets and runs it
IF THE BUILD FAILS
Read the first error line; fix the source or the board selection.
IF THE UPLOAD FAILS
Check the cable (data, not charge-only), the port and the board selection.
A successful upload proves the transfer worked — not that the behaviour is right.
Notes: TIME: 2 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: Can the chip directly read the same Arduino text that you type? KEY TAKEAWAY: Tools translate and package source into firmware, then upload it for the ESP32 to execute. DELIVERY: Walk the rail: source, compiler/toolchain, machine instructions, upload, execution. Libraries, linking and packaging are intentionally compressed into the build step. Upload commonly uses a USB path on the development board, which may be native USB or a USB-to-serial bridge. The boot process then starts the program. INTERACTION / ANSWER: No: the CPU executes machine instructions, not Arduino source text. A compile failure prevents a successful build; an upload failure prevents the new program reaching the board. A logic bug can remain even after both succeed. TRANSITION: Now become a detective: start with the physical evidence. TECHNICAL REFERENCES: Espressif, ESP32 Datasheet: https://documentation.espressif.com/esp32_datasheet_en.html 15 15 15 15

## Slide 16
PART 9 · DEBUGGING · SERIAL MONITOR AND ALTERNATIVES (OPTIONAL)
16 / 19
Investigate the physical system before you blame the code.
ASK IN ORDER
01
Is the board powered? (LED, USB, supply)
02
Are the connections correct? (pins, polarity, ground)
03
Is the expected code running? (right board, port, upload)
04
What does the Serial Monitor report? (baud rate matches)
SPOT THE BUG · 60 SECONDS
pinMode(LED_PIN, INPUT);
digitalWrite(LED_PIN, HIGH);
Wiring verified. Upload succeeded.
The LED never lights. Which word is wrong?
PLACEHOLDER
ESP32 on USB
PLACEHOLDER
Serial Monitor
Change one thing at a time. Observe, explain, then test again.
Disconnect power before rewiring. Serial output shows what the code sees, not whether wiring is safe.
SERIAL MONITOR · AND ALTERNATIVES
Serial.begin(115200);
Serial.println(reading);
Also: LED blink codes · text on the OLED
· a multimeter on the pin
Notes: TIME: 3 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: Before editing code, what physical evidence should a debugging detective inspect? KEY TAKEAWAY: Work from power and safe wiring toward software and observations. DELIVERY: Ask teams to silently spot the code issue, then compare with a neighbour. Always disconnect power before rewiring. Inspect supply voltage/current suitability, USB data cable and common reference where appropriate. Then verify the selected board/port, successful build/upload, expected sketch, and Serial Monitor settings and messages. INTERACTION / ANSWER: The example configures the LED pin as INPUT; for a verified active-high external LED output circuit it should be OUTPUT. Writing HIGH is not a substitute for configuring an output. Keep the resistor and correct polarity. Serial output helps observe execution; it cannot prove wiring is safe or correct. TRANSITION: Once the local behaviour works, communication can make it useful farther away. TECHNICAL REFERENCES: Espressif, Arduino-ESP32 GPIO API: https://docs.espressif.com/projects/arduino-esp32/en/latest/api/gpio.html 16 Answer: pinMode(LED_PIN, INPUT) should be OUTPUT for an LED driven by the pin. Writing HIGH does not configure the direction. 16 Answer: pinMode(LED_PIN, INPUT) should be OUTPUT for an LED driven by the pin. Writing HIGH does not configure the direction. PHOTO PLACEHOLDER: ESP32 on USB | Composition/crop: Three-quarter · cable and power LED visible · 4:3 | Caption: ESP32 connected by USB | Suggested search: ESP32 on USB | Recommended source: Own photo of the actual kit component | Replace with actual workshop hardware: Yes. PHOTO PLACEHOLDER: Serial Monitor | Composition/crop: Screenshot · readable lines · no private paths · 16:9 | Caption: Serial Monitor | Suggested search: Serial Monitor | Recommended source: Own photo of the actual kit component | Replace with actual workshop hardware: Yes. 16 SERIAL AND ALTERNATIVES: Serial.begin(115200) then Serial.println(value); the Monitor's baud rate must match. Alternatives when serial is unavailable: LED blink codes, printing to the OLED, a multimeter on the pin, or a logic analyser. Mark this part optional if time is short.

## Slide 17
PART 10 · IOT BASICS AND INTRODUCTION
17 / 19
A connected device is only useful
if someone can act on what it shares.
SENSOR
Observe the world
ESP32
Decide locally
WI-FI
Carry the message
WEB / CLOUD
Show status, keep history
USER
Take action
LOCAL OUTPUT
Buzzer or LED still responds if Wi-Fi drops
Smart alarm: the buzzer sounds locally; the dashboard adds context.
Traffic model: report the simulated event — never treat noise as authority.
Ask of every connected feature: who acts on this, and what happens when the network is down?
Notes: TIME: 2 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: If the Wi-Fi connection disappears, should a local smart alarm stop sounding? KEY TAKEAWAY: IoT connects a physical system to information and action, but connectivity must serve a real need. DELIVERY: Trace sensor to ESP32 to Wi-Fi to a web page or cloud service to user action. A local web page is possible; a cloud service is not mandatory. Communication can be two-way even though the slide shows a simple observation path. Retain the needed local function during network loss. Mention protecting credentials and considering privacy without opening a security lecture. INTERACTION / ANSWER: A locally required alarm should not depend unnecessarily on network availability. Uploading data alone does not make a system useful: somebody must understand or act on it. The traffic example remains a safe classroom simulation. TRANSITION: Let's see the smallest version of that on an ESP32: a web page served by the board itself. TECHNICAL REFERENCES: Espressif, Chip Series Comparison: https://docs.espressif.com/projects/esp-idf/en/v5.0-rc1/esp32/hw-reference/chip-series-comparison.html 17 17 17 17

## Slide 18
PART 11 · IOT ON THE ESP32 · SETTING UP A WEB SERVER
18 / 19
The ESP32 can serve a web page
that shows its own sensor reading.
webserver.ino · arduino-esp32
1 · JOIN THE NETWORK
WiFi.begin() joins the classroom Wi-Fi — or WiFi.softAP() makes the ESP32 its own hotspot.
2 · LISTEN ON PORT 80
WebServer waits for requests and the Serial Monitor prints the board's IP address.
3 · RESPOND
A laptop browser opens http://<board-ip>/ — the board replies with its live reading.
Facilitator demo · local network only — softAP mode needs no router, no internet and no phones.
#include <WiFi.h>
#include <WebServer.h>
WebServer server(80);
void setup() {
WiFi.begin(SSID, PASSWORD);
while (WiFi.status() != WL_CONNECTED)
delay(500);
server.on("/", []() {
server.send(200, "text/plain",
String(analogRead(POT_PIN)));
});
server.begin();
}
void loop() { server.handleClient(); }
Notes: TIME: 2.5 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: If the board can read a sensor, can it also show that reading to a browser on the same Wi-Fi? KEY TAKEAWAY: A few lines turn the ESP32 into a tiny web server: join a network, listen on port 80, reply to a request with live data. DELIVERY: Walk the three steps on the right while pointing at the matching code lines. WiFi.begin joins an existing network (station mode); WiFi.softAP creates the board's own hotspot so no campus network or internet is required. WebServer (arduino-esp32 library) listens on port 80; server.on("/") registers what to send back; server.handleClient() in loop() keeps answering. Print WiFi.localIP() (or softAPIP()) to the Serial Monitor so the class can see the address. This is a facilitator demo, not a student exercise — students do not need phones or internet. INTERACTION / ANSWER: Prediction — two laptops open the page at once: what happens? Both get a reply; the server answers requests one after another inside handleClient(), so the loop must keep running and must not block with long delays. Credentials belong in code you do not share on screen. TRANSITION: You now have every piece — sense, decide, act, and even share. Time to choose a problem worth solving. TECHNICAL REFERENCES: Espressif, Arduino-ESP32 Wi-Fi API: https://docs.espressif.com/projects/arduino-esp32/en/latest/api/wifi.html Espressif, arduino-esp32 WebServer library (bundled with the core): https://github.com/espressif/arduino-esp32/tree/master/libraries/WebServer

## Slide 19
TEAM DESIGN CHALLENGE · TWO MINUTES · THEN HANDS-ON
19 / 19
Design a system that senses, decides and acts.
02:00
At least one input
One decision rule
One output
Optional: connectivity
Then two teams share: the problem and the rule.
PHOTO PLACEHOLDER
Complete workshop kit — the actual components
Top-down flat lay · every part separated · 4:3
Don't just connect components —
make the system sense, decide, and act.
Notes: TIME: 4 minutes. Total teaching sequence: 45 minutes; checklist excluded. OPEN: With your team of five, what useful system can you design from this kit? KEY TAKEAWAY: Start with a problem and a decision rule, not a random pile of components. DELIVERY: Four minutes total: 15 seconds brief, two minutes team design, two shares of 30 seconds, and 45 seconds transition. There are approximately 50 students in 10 teams of five. Assign quick roles if helpful: problem owner, input chooser, rule writer, output chooser, spokesperson. No phones or internet are needed. Before powering hardware, have the wiring and power plan checked. INTERACTION / ANSWER: A valid design names at least one input, a testable rule and one output; connectivity is optional. Example: a potentiometer threshold controls a buzzer smart alarm. Example: a button simulates an ambulance event and changes a tabletop LED traffic pattern. Two teams share; ask what happens if an input is missing or wrong. TRANSITION: Say the closing line exactly, then begin the board-specific hands-on instructions. End the audience slideshow here; the final checklist is presenter reference only. 18 PHOTO PLACEHOLDER: Complete workshop kit — the actual components | Composition/crop: Top-down flat lay · every part separated · 4:3 | Caption: The workshop kit | Suggested search: Complete workshop kit — the actual components | Recommended source: Own photo of the actual kit component | Replace with actual workshop hardware: Yes. 18

## Slide 20
PRESENTER REFERENCE · NOT PART OF THE 45 MINUTES
REF
Image checklist
PH = photo placeholder. Full subjects, compositions, crops and search phrases are in these notes.
Slide | Image | Status | Search | Source | Kit?
1 | Objects | PH | Objects | Stock/CC | No
5 | Board | PH | Board | Own/maker | Yes
9 | Sensors | PH | Sensors | Own | Yes
10 | Outputs | PH | Outputs | Own | Yes
12 | Button/LED | PH | Button/LED | Own | Yes
13 | Pot/LDR | PH | Pot/LDR | Own | Yes
16 | USB/IDE | PH | USB/IDE | Own | Yes
19 | Kit | PH | Kit | Own | Yes
Notes: IMAGE CHECKLIST — presenter reference only (0 minutes). The authoring interface cannot hide a slide, so this stays a visible appendix: end the audience presentation after slide 19. All photo slots are deliberate placeholders — no accessible, verified photograph could be inserted and no AI-generated hardware images are used. The cover/closing backdrop is an AI-generated abstract light texture. No animations were added; pacing cues are in the notes. Slide 1 | Image required: Collage of six everyday objects (traffic light, smartwatch, washing machine, car dashboard, elevator panel, smart speaker) | Status: Placeholder | Suggested search phrase: Collage of six everyday objects (traffic light, smartwatch, washing machine, car dashboard, elevator panel, smart speaker) | Recommended source type: Licensed stock / verified CC or public-domain photos | Replace with actual workshop hardware: No | Composition/crop: Six real photographs, 4:3 each, arranged 3 × 2 | Caption: Everyday objects that quietly contain microcontrollers. Slide 5 | Image required: ESP32 development board — the exact kit model | Status: Placeholder | Suggested search phrase: ESP32 development board — the exact kit model | Recommended source type: Own photo of the actual kit component | Replace with actual workshop hardware: Yes | Composition/crop: Top-down · USB connector visible · space for callouts · 4:3 | Caption: ESP32 development board. Slide 9 | Image required: Push button | Status: Placeholder | Suggested search phrase: Push button | Recommended source type: Own photo of the actual kit component | Replace with actual workshop hardware: Yes | Composition/crop: Top-down · legs visible · 4:3 | Caption: Push button. Slide 9 | Image required: LDR module | Status: Placeholder | Suggested search phrase: LDR module | Recommended source type: Own photo of the actual kit component | Replace with actual workshop hardware: Yes | Composition/crop: Top-down · LDR visible · 4:3 | Caption: LDR module. Slide 9 | Image required: Microphone module | Status: Placeholder | Suggested search phrase: Microphone module | Recommended source type: Own photo of the actual kit component | Replace with actual workshop hardware: Yes | Composition/crop: Top-down · mic visible · 4:3 | Caption: Microphone module. Slide 9 | Image required: Ultrasonic sensor | Status: Placeholder | Suggested search phrase: Ultrasonic sensor | Recommended source type: Own photo of the actual kit component | Replace with actual workshop hardware: Yes | Composition/crop: Front · transducers visible · 4:3 | Caption: Ultrasonic sensor. Slide 9 | Image required: DHT sensor | Status: Placeholder | Suggested search phrase: DHT sensor | Recommended source type: Own photo of the actual kit component | Replace with actual workshop hardware: Yes | Composition/crop: Front · connector visible · 4:3 | Caption: DHT sensor. Slide 10 | Image required: LED | Status: Placeholder | Suggested search phrase: LED | Recommended source type: Own photo of the actual kit component | Replace with actual workshop hardware: Yes | Composition/crop: Macro · both leads · 4:3 | Caption: LED. Slide 10 | Image required: Buzzer | Status: Placeholder | Suggested search phrase: Buzzer | Recommended source type: Own photo of the actual kit component | Replace with actual workshop hardware: Yes | Composition/crop: Top-down · connector · 4:3 | Caption: Buzzer. Slide 10 | Image required: OLED display | Status: Placeholder | Suggested search phrase: OLED display | Recommended source type: Own photo of the actual kit component | Replace with actual workshop hardware: Yes | Composition/crop: Front · whole module · 4:3 | Caption: OLED display. Slide 10 | Image required: Micro servo | Status: Placeholder | Suggested search phrase: Micro servo | Recommended source type: Own photo of the actual kit component | Replace with actual workshop hardware: Yes | Composition/crop: Side · horn + cable · 4:3 | Caption: Micro servo. Slide 12 | Image required: Push button | Status: Placeholder | Suggested search phrase: Push button | Recommended source type: Own photo of the actual kit component | Replace with actual workshop hardware: Yes | Composition/crop: Top-down · legs visible · 4:3 | Caption: Push button. Slide 12 | Image required: LED | Status: Placeholder | Suggested search phrase: LED | Recommended source type: Own photo of the actual kit component | Replace with actual workshop hardware: Yes | Composition/crop: Macro · both leads visible · 4:3 | Caption: LED. Slide 13 | Image required: Potentiometer | Status: Placeholder | Suggested search phrase: Potentiometer | Recommended source type: Own photo of the actual kit component | Replace with actual workshop hardware: Yes | Composition/crop: Three-quarter view · shaft and terminals visible · 4:3 | Caption: Potentiometer. Slide 13 | Image required: LDR module | Status: Placeholder | Suggested search phrase: LDR module | Recommended source type: Own photo of the actual kit component | Replace with actual workshop hardware: Yes | Composition/crop: Top-down · sensor and connector visible · 4:3 | Caption: LDR module. Slide 16 | Image required: ESP32 on USB | Status: Placeholder | Suggested search phrase: ESP32 on USB | Recommended source type: Own photo of the actual kit component | Replace with actual workshop hardware: Yes | Composition/crop: Three-quarter · cable and power LED visible · 4:3 | Caption: ESP32 connected by USB. Slide 16 | Image required: Serial Monitor | Status: Placeholder | Suggested search phrase: Serial Monitor | Recommended source type: Own photo of the actual kit component | Replace with actual workshop hardware: Yes | Composition/crop: Screenshot · readable lines · no private paths · 16:9 | Caption: Serial Monitor. Slide 19 | Image required: Complete workshop kit — the actual components | Status: Placeholder | Suggested search phrase: Complete workshop kit — the actual components | Recommended source type: Own photo of the actual kit component | Replace with actual workshop hardware: Yes | Composition/crop: Top-down flat lay · every part separated · 4:3 | Caption: The workshop kit.